## Slide 1: Network Layer: IPv4 Functions
Lecture 8 | Part 1 | CSE421 – Computer Networks
Department of Computer Science and Engineering School of Data & Science

## Slide 2: Objectives
Short overview of the Network Layer
Virtual Circuits & Datagram Networks
IP Fragmentation & Reassembly
ICMP
  Ping
  Traceroute

## Slide 3: The Network Layer
Transport segment from sending to receiving host
On sending side encapsulates segments into packets
Network layer protocols in every host, router
Router examines header fields in all IP packets passing through it
On receiving side, delivers segments to transport layer
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical

## Slide 4: Functions of Network Layer
Forwarding: move packets from router’s input to appropriate router output
  Analogy: process of getting through a single interchange
Routing: determine route taken by packets from source to destination
  Analogy: process of planning trip from source to dest
  Has various routing algorithms
1
2
3
0111
value in arriving
packet’s header
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1

## Slide 5: Virtual Circuits Datagram Network

## Slide 6: Connection and connection-less service
Datagram network => network-layer connectionless service
VC network => network-layer connection service
  analogous to the transport-layer services, but:
  service: host-to-host
  no choice: network provides one or the other
  implementation: in network core

## Slide 7: Datagram networks
No call setup at network layer
Routers: no state about end-to-end connections
  no network-level concept of “connection”
Packets forwarded using destination host address
  packets between same source-dest pair may take different paths
application
transport
network
data link
physical
application
transport
network
data link
physical
1. Send data
2. Receive data

## Slide 8: Virtual circuits: signaling protocols
Used to setup, maintain teardown VC
Used in ATM, frame-relay, X.25
Not used in today’s Internet
application
transport
network
data link
physical
application
transport
network
data link
physical
1. Initiate call
2. incoming call
3. Accept call
4. Call connected
5. Data flow begins
6. Receive data

## Slide 9: Functions of Router
Run routing algorithms/protocol (RIP, OSPF, BGP)
Forwarding datagrams from incoming to outgoing link
Decentralized switching:
  Given datagram dest., lookup output port using forwarding table in input port memory
  Goal: complete input port processing at ‘line speed’
  Queuing: if datagrams arrive faster than forwarding rate into switch fabric
Physical layer:
bit-level reception
Data link layer:
e.g., Ethernet
see chapter 5

## Slide 10: Internet Protocol

## Slide 11: Internet Network Layer
Host, router network layer functions:
forwarding
table
Routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
datagram format
packet handling conventions
ICMP protocol
error reporting
router “signaling”
Transport layer: TCP, UDP
Link layer
physical layer
Network
layer

## Slide 12: IPv4 Datagram Format

## Slide 13: Network Layer: IPv4 Functions
Lecture 8 | Part 2 | CSE421 – Computer Networks
Department of Computer Science and Engineering School of Data & Science

## Slide 14: IP Fragmentation & Reassembly
network links have MTU (max.transfer size) - largest possible link-level frame.
  different link types, different MTUs
large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
  “reassembled” only at final destination
  IP header bits used to identify, order related fragments
fragmentation:
in: one large datagram (4000 bytes)
out: 3 smaller datagrams
reassembly
Link MTU: 1500bytes

## Slide 15: IP Fragmentation & Reassembly
Example:
  4000 Bytes of datagram
  MTU = 1500 Bytes
    Header + Data
    Header size is usually 20 bytes
      It can differ
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
One large datagram becomes
several smaller datagrams
1480 bytes in data field
offset =
1480/8

## Slide 16: IP Fragmentation & Reassembly
Data Bytes | Fragment Offset
0 -1479 | 0/8=0
1480-2959 | 1480/8=185
2960-4439 | 2960/8=370
4440-5119 | 4440/8=555

## Slide 17: IP Fragmentation Example

## Slide 18: Network Layer: IPv4 Functions
Lecture 8 | Part 3 | CSE421 – Computer Networks
Department of Computer Science and Engineering School of Data & Science

## Slide 19: ICMP

## Slide 20: ICMP
Also known as Internet Control Message Protocol
It is chiefly used by the operating systems in IP network management and administration.
Used for
  errors in the underlying communications of network applications
  availability of remote hosts
  network congestion
It does not carry application data, but rather information about the status of the network itself.
Example of ICMP in practice
  PING
  TRACEROUTE

## Slide 21: Ping
Utility used to test the reachability of a host.
Sends Internet Control Message Protocol (ICMP) echo request packets to the target host and waiting for an ICMP response.
In the process it measures the time from transmission to reception (round-trip time) and records any packet loss.

## Slide 22: ICMP Message
ICMP message: type, code plus first 8 bytes of IP datagram causing error

## Slide 23: Ping Attacks
ICMP PING flood attack /DOS Attack :
  It uses the ICMP echo command to flood large amounts of data packets to the victim’s computer in an attempt to overload it.
  Another type of DOS Attack : Deny to give service by replying with false message.

## Slide 24: Ping Attacks
ICMP DDOS attack – Zombie Attack:
  Much like the ping flood method, only multiple computers are being used. In this instance, the computers that are being used may or may not be aware of the fact that they are attacking a website or network. Trojans and viruses commonly give the hacker control of a computer, and thus, the ability to use them for attack. In this case the victim computers are called zombies.

## Slide 25: Ping Attacks
ICMP DDOS attack – Packet magnification (or ICMP Smurf):
  An attacker sends forged ICMP echo packets to vulnerable networks' broadcast addresses. All the systems on those networks send ICMP echo replies to the victim.

## Slide 26: Traceroute
Tool used to trace path from source to destination host.
The IP address and domain name (if there is one) of each router is returned to the client.
Commands:
  Unix: traceroute
  Cisco IOS: traceroute (trace)
  DOS: tracert
Hop 1: User LAN router
Hops 2-7: Verizon (ISP) network
Hops 8-10: the Yahoo LAN

## Slide 27: Traceroute: Another example
Hop 1: User LAN router
Hops 2-4: Verizon network (a backbone ISP)
Hops 5-6: Alternet (a backbone ISP)
Hops 7-11: Level 3 (a backbone ISP)
Hops 12-14: the Google LAN

## Slide 28: Traceroute: Request Timed Out
This message indicates that the router security settings keep it from revealing its identity or the router and connection are slow.

## Slide 29: Traceroute
Source sends series of UDP segments to dest
  First has TTL =1
  Second has TTL=2, etc.
  Unlikely port number
When nth datagram arrives to nth router:
  Router discards datagram
  And sends to source an ICMP message (type 11, code 0)
  Message includes name of router& IP address
When ICMP message arrives, source calculates RTT
Traceroute does this 3 times
Stopping criterion
  UDP segment eventually arrives at destination host
  Destination returns ICMP “port unreachable” packet (type 3, code 3)
    When source gets this ICMP, it stops.

## Slide 30: Traceroute
How it works by fooling the routers & host!
  Trace uses ping (echo requests)
  Traceroute sets the TTL (Time to Live) field, in the Layer 3 (IP) header, initially to “1”.
Layer 2 Header | Layer 3 Header | ICMP Message Echo Request (trace) |  | Layer 4 Header (UDP) | Layer 2 Trailer
*All layer 2 info | Src. IP: 10.0.0.1 Dest. IP: 192.168.10.2 TTL = 1 | Type: 8 Code: 0 | Other fields of ICMP Packet | Dest. Port: 35,000 | FCS

## Slide 31: Traceroute
RTB - TTL:
  When a router receives an IP Packet, it decrements the TTL by 1.
    TTL ‘1’ is decremented to ‘0’
  If the TTL is 0, it will not forward the IP Packet, and send back to the source with an ICMP “time exceeded” message.
Layer 2 Header | Layer 3 Header | ICMP Message (Time Exceeded) |  | Layer 4 Header (UDP) | Layer 2 Trailer
*All layer 2 info | Src. IP: 10.0.0.2 Dest. IP: 10.0.0.1 | Type: 11 Code: 0 | Other fields of ICMP Packet | - | FCS

## Slide 32: Traceroute
RTA at this point
  The traceroute program of the sending host (RTA) will use the source IP address of this ICMP Time Exceeded packet to display the following at the first hop.
Output of RTA: 1 10.0.0.2 4 msec 4 msec 4 msec
Layer 2 Header | Layer 3 Header | ICMP Message (Time Exceeded) |  | Layer 4 Header (UDP) | Layer 2 Trailer
*All layer 2 info | Src. IP: 10.0.0.2 Dest. IP: 10.0.0.1 | Type: 11 Code: 0 | Other fields of ICMP Packet | - | FCS

## Slide 33: Traceroute
RTA
  The traceroute program increments the TTL by 1 (now 2 ) and resends the ICMP Echo Request packet.
Layer 2 Header | Layer 3 Header | ICMP Message Echo Request (trace) |  | Layer 4 Header (UDP) | Layer 2 Trailer
*All layer 2 info | Src. IP: 10.0.0.1 Dest. IP: 192.168.10.2 TTL = 2 | Type: 8 Code: 0 | Other fields of ICMP Packet | Dest. Port: 35,000 | FCS

## Slide 34: Traceroute
This time RTB decrements the TTL by 1 and it is NOT 0. (It is 1.)
So it looks up the destination IP address in its routing table and forwards it on to the next router.
Layer 2 Header | Layer 3 Header | ICMP Message Echo Request (trace) |  | Layer 4 Header (UDP) | Layer 2 Trailer
*All layer 2 info | Src. IP: 10.0.0.1 Dest. IP: 192.168.10.2 TTL = 1 | Type: 8 Code: 0 | Other fields of ICMP Packet | Dest. Port: 35,000 | FCS

## Slide 35: Traceroute
RTC decrements the TTL by 1 and it is 0.
  RTC notices the TTL is 0 and sends back the ICMP Time Exceeded message back to the source.
  RTC’s IP header includes its own IP address (source IP) and the sending host’s IP address (destination IP address of RTA).
  The sending host, RTA, will use the source IP address of this ICMP Time Exceeded message to display at the second hop.
Layer 2 Header | Layer 3 Header | ICMP Message (Time Exceeded) |  | Layer 4 Header (UDP) | Layer 2 Trailer
*All layer 2 info | Src. IP: 172.16.0.2 Dest. IP: 10.0.0.1 | Type: 11 Code: 0 | Other fields of ICMP Packet | - | FCS
1 10.0.0.2 4 msec 4 msec 4 msec
2 172.16.0.2 20 msec 16 msec 16 msec

## Slide 36: Traceroute
The sending host, RTA:
  The traceroute program increments the TTL by 1 (now 3 ) and resends the Packet.
Layer 2 Header | Layer 3 Header | ICMP Message Echo Request (trace) |  | Layer 4 Header (UDP) | Layer 2 Trailer
*All layer 2 info | Src. IP: 10.0.0.1 Dest. IP: 192.168.10.2 TTL = 3 | Type: 8 Code: 0 | Other fields of ICMP Packet | Dest. Port: 35,000 | FCS

## Slide 37: Traceroute
RTB
  This time RTB decrements the TTL by 1 and it is NOT 0. (It is 2.)
  So it looks up the destination IP address in its routing table and forwards it on to the next router.
Layer 2 Header | Layer 3 Header | ICMP Message Echo Request (trace) |  | Layer 4 Header (UDP) | Layer 2 Trailer
*All layer 2 info | Src. IP: 10.0.0.1 Dest. IP: 192.168.10.2 TTL = 2 | Type: 8 Code: 0 | Other fields of ICMP Packet | Dest. Port: 35,000 | FCS

## Slide 38: Traceroute
RTC
  This time RTC decrements the TTL by 1 and it is NOT 0. (It is 1.)
  So it looks up the destination IP address in its routing table and forwards it on to the next router.
Layer 2 Header | Layer 3 Header | ICMP Message Echo Request (trace) |  | Layer 4 Header (UDP) | Layer 2 Trailer
*All layer 2 info | Src. IP: 10.0.0.1 Dest. IP: 192.168.10.2 TTL = 1 | Type: 8 Code: 0 | Other fields of ICMP Packet | Dest. Port: 35,000 | FCS

## Slide 39: Traceroute
RTD decrements the TTL by 1 and it is 0.
However, RTD notices that the Destination IP Address of 192.168.0.2 is it’s own interface.
Since it does not need to forward the packet, the TTL of 0 has no affect.
RTD sends the packet to the UDP process.
UDP examines the unrecognizable port number of 35,000 and sends back an ICMP Port Unreachable message to the sender, RTA, using Type 3 and Code 3.
Layer 2 Header | Layer 3 Header | ICMP Message (Port Unreachable) |  | Layer 4 Header (UDP) | Layer 2 Trailer
*All layer 2 info | Src. IP: 192.168.10.2 Dest. IP: 10.0.0.1 | Type: 3 Code: 3 | Other fields of ICMP Packet | - | FCS

## Slide 40: Traceroute
Sending host, RTA
  RTA receives the ICMP Port Unreachable message.
  The traceroute program uses this information (Source IP Address) and displays the third hop.
  The traceroute program also recognizes this Port Unreachable message as meaning this is the destination it was tracing.
Layer 2 Header | Layer 3 Header | ICMP Message (Port Unreachable) |  | Layer 4 Header (UDP) | Layer 2 Trailer
*All layer 2 info | Src. IP: 192.168.10.2 Dest. IP: 10.0.0.1 | Type: 3 Code: 3 | Other fields of ICMP Packet | - | FCS

## Slide 41: 3D Traceroute

## Slide 42: The End