## Slide 1: Network Layer: IPv4 Addressing
Lecture 9 | Part 1 | CSE421 – Computer Networks
Department of Computer Science and Engineering School of Data & Science

## Slide 2: Objectives
Anatomy of IPv4 Address
  Subnet/Prefix Mask
Types of Address
  Network
  Host
  Broadcast
Specific Address
  Unicast
  Multicast
  Broadcast
Classful IP Addressing

## Slide 3: Anatomy of IPv4

## Slide 4: Anatomy of an IPv4 Address
Each device on a network must be uniquely identified at the Network layer.
For IPv4, a 32 bit source and destination address is contained in each packet.

## Slide 5: IPv4 Addressing Structure

## Slide 6: Anatomy of an IPv4 Address
Dotted decimals
Network part
Host part
32 bits
Divided into 4 Octets

## Slide 7: Binary to decimal and Vice Versa

## Slide 8: Networks and Hosts
To identify a path or "route" through a network, the address must be composed of two parts:
  Network portion
  Host portion
1.1
1.2
1.3
2.1
2.2
3.1
3.2

## Slide 9: Network Portion
Network Portion:
  Some portion of the high-order bits
  A network can be defined as a group of hosts that have identical bit patterns in the network address portion of their addresses.
192.168.1.2 | 11000000 | 10101000 | 00000001 | 00000010
192.168.1.67 | 11000000 | 10101000 | 00000001 | 01000011
192.168.1.204 | 11000000 | 10101000 | 00000001 | 11001100

## Slide 10: Network Portion
Host Portion:
  A variable number of least significant bits that are called the host portion of the address.
  The number of bits used in this host portion determines the number of hosts that we can have within the network.
192.168.1.2 | 11000000 | 10101000 | 00000001 | 00000010
192.168.1.67 | 11000000 | 10101000 | 00000001 | 01000011
192.168.1.204 | 11000000 | 10101000 | 00000001 | 11001100

## Slide 11: Prefix Mask
How do we or devices identify the network part or the host part?
Answer: Using the “Prefix Mask”.
192.168.10.2/24
  Means that the first 24 bits are the network portion.
  The last 8 bits are the host portion.
Subnet Mask; the other form of “Prefix Mask”.
  Prefix length of /24 means a subnet mask of 255.255.255.0

## Slide 12: Subnet Mask
The Prefix Mask and the Subnet Mask are different ways of representing the same information.
Examples:
  Prefix Mask of /24 or a subnet mask of 255.255.255.0
  Prefix Mask of /16 or a subnet mask of 255.255.0.0
  Prefix Mask of /8 or a subnet mask of 255.0.0.0
Conversion:
  Subnet mask has the same format as an IP address. Hence, it has 32 bits divided into 8 bits (octets)
  Prefix mask of /24 means, the first (MSB) 24 bits of subnet mask would be 1
  Binary: 11111111.11111111.11111111.00000000
Decimal: 255 . 255 . 255 . 0

## Slide 13: Exercise
What’s the subnet mask of the following?
  IP Address: 10.24.36.2 / 4
  IP Address: 10.24.36.2 / 12
  IP Address: 10.24.36.2 / 16
  IP Address: 10.24.36.2 / 23
What’s the prefix mask of the following?
  IP Address: 10.24.36.2; Subnet Mask: 255.255.224.0
  IP Address: 10.24.36.2; Subnet Mask: 255.255.255.192
  IP Address: 10.24.36.2; Subnet Mask: 255.255.255.252
  IP Address: 10.24.36.2; Subnet Mask: 255.254.0.0
  IP Address: 10.24.36.2; Subnet Mask: 255.255.240.0

## Slide 14: ANDing the Binaries
Inside data network devices, digital logic is applied for their interpretation of the addresses.
AND is used in determining the network address.
  0 AND 0 = 0
  1 AND 0 = 0
  1 AND 1 = 1
  0 AND 1 = 0
 | Decimal | Binary
IP Address | 135.15.2.1 | 10000111 00001111 00000010 00000001
Subnet Mask | 255.255.0.0 | 11111111 11111111 00000000 00000000
Network Address | 135.15.0.0 | 10000111 00001111 00000000 00000000

## Slide 15: But Why AND?
Routers use the ANDing process to determine the route a packet will take.
The network number of the destination address is used to find the network in the routing table.
The router then determines the best path for the frame.

## Slide 16: Network Layer: IPv4 Addressing
Lecture 9 | Part 2 | CSE421 – Computer Networks
Department of Computer Science and Engineering School of Data & Science

## Slide 17: Types of Addresses

## Slide 18: Types of address
Every network has
  Network Address – The first IP in the range
  Broadcast Address – The second IP in the range
  Host Addresses – Everything in between

## Slide 19: The Addresses
Network Address
  All hosts in the network will have the same network bits.
  Cannot be assigned to a device.
  Each host bit in this address will be 0.
Broadcast Address
  Cannot be assigned to a device.
  Each host bit in this address will be 1.
Host Address
  The unique address assigned to each device on the network.
  For a network of 192.168.10.0/24
    Addresses 192.168.10.1 through 192.168.10.254 are all host addresses

## Slide 20: The Addresses at a Glance
Say, you have a random IP address 192.168.10.193/24

## Slide 21: Network Prefix
The network prefix is not always /24.

## Slide 22: Network Layer: IPv4 Addressing
Lecture 9 | Part 3 | CSE421 – Computer Networks
Department of Computer Science and Engineering School of Data & Science

## Slide 23: Special Addresses

## Slide 24: Special Addresses
Unicast
  A message addressed to one host
Broadcast
  A message addressed to all hosts on a network.
  Uses network’s broadcast address or 255.255.255.255 locally
Multicast
  A message addressed to a group of hosts.
  Uses an IP address starting with 224 - 239

## Slide 25: Unicast

## Slide 26: Broadcast Address
Limited Broadcast
Directed Broadcast
  For a host outside of the network to communicate with the hosts within the 172.16.4.0 /24 network, the destination address of the packet would be 172.16.4.255.

## Slide 27: Multicast
Examples of Multicast Application
  Video and audio broadcasts
  Routing information exchange by routing protocols
  Distribution of software
  News feeds

## Slide 28: Classful Addressing

## Slide 29: Classful Addressing

## Slide 30: Classful Networks : Range
Address class | First octet range | Number of networks | Hosts per network
Class A | 0 to 127 | 128 (less 0 and 127) | 16,777,214
Class B | 128 to 191 | 16,348 | 65,534
Class C | 192 to 229 | 2,097,152 | 254

## Slide 31: The End