## Slide 1: Network Layer: Subnetting
Lecture 10 | Part 1| CSE421 – Computer Networks
Department of Computer Science and Engineering School of Data & Science

## Slide 2: Objectives
Subnetting
VLSM
  Binary Calculation
  Base 256 Calculation
Route Summarization

## Slide 3: IPv4 Address Exhaustion

## Slide 4: Solutions
Long term:
  Change to IP version 6.
  Plenty of addresses using a different scheme
Short term:
  Use Subnetting (VLSM & CIDR) to avoid wasting addresses
  Use private addresses locally and NAT for internet access – lets many host share a few public addresses
  DHCP!

## Slide 5: Subnetting
The strategy used to partition a single physical network into more than one smaller logical sub-networks (subnets).
Subnets are designed by accepting bits from the IP address's host part and using these bits to assign a number of smaller sub-networks inside the original network.
Allows an organization to add sub-networks without the need to acquire a new network number via the Internet service provider (ISP).

## Slide 6: Subnetting
Three methods of subnetting
  Classful IP Addressing – We have already seen it in the previous lecture!
  Fixed Length Subnet Masking
  Variable Length Masking
Goal
  Assign a block of IP addresses to fulfill the total needs of a network
    A network has 200 hosts per say, give them a network address which can support 200 hosts!
    Give them the smallest block possible to waste least of the IP addresses but not below 200!
**Note: You can assign blocks of size 2N only. This is because the number of bits assigned to host from an IP address cannot be partial, number of bits is discrete and must be an integer value. (Can you assign 1.5 bits to host and 30.5 bits to network?)

## Slide 7: Network Layer: Subnetting
Lecture 10 | Part 2 | CSE421 – Computer Networks
Department of Computer Science and Engineering School of Data & Science

## Slide 8: Fixed length subnetting
All subnets of a main network must have the same subnet mask.
This means that they must all have the same number of hosts.
Example
  How many network addresses do you need for the organization?
  How many network addresses do you have?
  How many bits do you have for hosts?
  How many host bits do you need to borrow to create the number of sub networks that you need?
Banani Branch
15 Hosts
Khulna Branch
120 Hosts
Motijheel Branch
30 Hosts

## Slide 9: Fixed Length Subnetting: Example
192.168.80.0/27
192.168.80.32/27
192.168.80.64/27
192.168.80.96/27
192.168.80.128/27
192.168.80.160/27
192.168.80.192/27
192.168.80.0/24

## Slide 10: VLSM
Also known as “Variable Length Subnet Masking”
Always satisfy the requirements of your biggest LAN and then work your way down to the smallest LAN.
  Assign a block of IP satisfying only that particular LAN.
    200 hosts? Assign a block of size 256 IPs!
    1000 hosts? Assign a block of size 1024 IPs!
    2 Hosts? Assign a block of size 2 IPs!

## Slide 11: Comparison of Subnetting
Given the network 192.168.1.0/24.
  Subnet this to two hosts of size 120 (Network A) and 3 (Network B)
  So, Network A needs 122 IPs and Network B needs 5 IPs.
Classful IP Addressing |  | Fixed Length Subnet Masking |  | Variable Length Subnet Masking (VLSM)/CIDR | 
Network A: Subnet; Class C: Waste: 254 – 122 | 122 -254 132 | Network A: Subnet Size(27): Waste: 128 – 122 | 122 -128 6 | Network A: Subnet Size(27): Waste: 128 – 122 | 122 -128 6
Network B: Subnet; Class C: Waste: 254 – 5 | 5 -254 249 | Network B: Subnet Size(27): Waste: 128 – 5 | 5 -128 123 | Network B: Subnet Size(23): Waste: 128 – 5 | 5 -8 3
Total Waste: | 381 | Total Waste: | 129 | Total Waste: | 9
**Total Waste = WasteNetwork A + WasteNetwork B
**WasteNetwork Y = Subnet SizeNetwork Y – Network YHost

## Slide 12: Comparison of Subnetting
Given the network 192.168.1.0/24.
  Subnet this to two hosts of size 120 (Network A) and 3 (Network B)
  So, Network A needs 122 IPs and Network B needs 5 IPs.
**Total Waste = WasteNetwork A + WasteNetwork B
**WasteNetwork Y = Subnet SizeNetwork Y – Network YHost
Classful IP Addressing
Fixed Length Subnet
Masking
Variable Length Subnet
Masking (VLSM)/CIDR
Network A:
Subnet; Class C:
Waste: 254
–
122
122
-
256
134
Network A:
Subnet Size(2
7
):
Waste: 128
–
122
122
-
128
6
Network A:
Subnet Size(2
7
):
Waste: 128
–
122
122
-
128
6
Network B:
Subnet; Class C:
Waste: 254
–
5
5
-
256
251
Network B:
Subnet Size(2
7
):
Waste: 128
–
5
5
-
128
123
Network B:
Subnet Size(2
3
):
Waste: 128
–
5
5
-
8
3
Total Waste:
385
Total Waste:
129
Total Waste:
9

## Slide 13: Lots of Waste!
Waste:
  Classful subnetting wastes addresses.
  If you are using private addresses then you may not be bothered.
  Waste of public addresses does matter.
Solutions:
  Variable Length Subnet Masking (VLSM)
  Create subnets as per specific host requirements.

## Slide 14: Network Layer: Subnetting
Lecture 10 | Part 3 | CSE421 – Computer Networks
Department of Computer Science and Engineering School of Data & Science

## Slide 15: VLSM Example 1

## Slide 16: VLSM Example 2
4 LANs
3 WANs
1 Switched Network

## Slide 17: Network Layer: Subnetting
Lecture 10 | Part 4 | CSE421 – Computer Networks
Department of Computer Science and Engineering School of Data & Science

## Slide 18: CIDR Concept
Also known as “Classless Inter-Domain Routing”
To CIDR-compliant routers, address class is meaningless
The network portion of the address is determined by the network subnet mask, also known as the prefix or prefix length (/8, /19, etc.)
Classless routing protocols are complaint with CIDR which means they understand
  VLSM and
  Route Summarization.
All routing protocols are classless nowadays.

## Slide 19: The End