## Slide 1: Network Layer Routing Algorithm Distance Vector Routing
Lecture 13 | Part 1| CSE421 – Computer Networks
Department of Computer Science and Engineering School of Data & Science

## Slide 2: Objectives
understand principles behind network layer services:
  network layer service models
  forwarding versus routing
  how a router works
  routing algorithms
    distance vector
    link state
    hierarchical routing
  broadcast, multicast

## Slide 3: Popular Routing Protocols

## Slide 4: Autonomous Systems
Internet is divided into autonomous systems.
An autonomous system (AS) is a group of networks and routers under the authority of a single administration.
Routing inside an autonomous system is called intra-domain routing. Routing between autonomous systems is called inter-domain routing.

## Slide 5: Autonomous Systems
RIP/ OSPF

## Slide 6: Routing Algorithms
Given a set of routers and links connecting the routers.
Routing algorithm finds a “good” path from the source to destination router.
Good path = Least cost path

## Slide 7: Routing Algorithm classification
Static or dynamic?
Static:
routes change slowly over time
Manually configured
Dynamic:
routes change more quickly
  in response to link cost changes

## Slide 8: Routing Algorithm classification
Global or Decentralized
Global:
all routers have complete topology and link cost info
“link state” algorithms
Decentralized:
router knows physically-connected neighbors, link costs to neighbors
iterative process of computation, exchange of info with neighbors
“distance vector” algorithms

## Slide 9: Routing on a Graph
Essentially a graph theory problem
  Network is a directed graph; routers are vertices
Find “best” path between every pair of vertices
  In the simplest case, best path is the shortest path

## Slide 10: Graph abstraction
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
Graph: G = (N,E)
N = set of routers = { u, v, w, x, y, z }
E = set of links ={ (u,v), (u,x), (u,w), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z) }
Notes: 10

## Slide 11: Graph abstraction: costs
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
c(x,x’) = cost of link (x,x’)
- e.g., c(w,z) = 5
Question: What’s the least-cost path between u and z ?
Routing algorithm: algorithm that finds least-cost path

## Slide 12: Distance Vector Algorithm

## Slide 13: Distance Vector Algorithm
Distributed:
each node receives info from one or more of its directly connected neighbors
Performs a calculations
Distributes the results back to its neighbors
Iterative
Process continues until no more info to exchange
Asynchronous:
All nodes operate independently
Notes: 13

## Slide 14
Distance Vector Algorithm

## Slide 15: Distance Vector Algorithm
Bellman-Ford Equation Algorithm
computes shortest paths from a single source vertex to all of the other vertices in a weighted digraph.
Distributed route computation using only neighbor’s info

## Slide 16: Distance Vector Algorithm
Objective:
dx(y) := cost of least-cost path from x to y
Then
where min is taken over all neighbors v of x
dx(y) = min v {c(x,v) + dv(y) }

## Slide 17: Distance Vector Algorithm
With the Distance Vector Routing algorithm, the node x contains the following routing information:
For each neighbor v, the cost c(x,v) is the path cost from x to directly attached neighbor, v.
The distance vector x, i.e., Dx = [ Dx(y) : y in N ], containing its cost to all destinations, y, in N.
The distance vector of each of its neighbors, i.e., Dv = [ Dv(y) : y in N ] for each neighbor v of x.

## Slide 18: Bellman-Ford example from u to z
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
Clearly, dv(z) = 5, dx(z) = 3, dw(z) = 3
du(z) = min { c(u,v) + dv(z),
c(u,x) + dx(z),
c(u,w) + dw(z) }
= min {2 + 5,
1 + 3,
5 + 3} = 4
  Node that achieves minimum is the next hop in shortest path to a destination,
  To go to z from u, x in the next hop in the forwarding table
B-F equation says:
U has 3 neighbors v, x and w

## Slide 19: Distance vector algorithm
Basic idea:
Each node periodically sends its own distance vector estimate to neighbors
When a node x receives new DV estimate from neighbor;
It updates its own DV using B-F equation:
Notes: 19

## Slide 20
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0
from
cost to
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
time
x
z
1
2
7
y
node x table
node y table
node z table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
3
2

## Slide 21
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0
from
cost to
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
time
x
z
1
2
7
y
node x table
node y table
node z table
Dy(x) = min{c(y,x) + Dx(x), c(y,z) + Dz(x)} = min{2+0 , 1+7} = 2
Dy(z) = min{c(y,x) + Dx(z), c(y,z) + Dz(z)}
= min{2+7 , 1+0} = 1
3
2
x y z
x
y
z
0 2 7
1
7 1 0
2
0

## Slide 22
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0
from
cost to
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
time
x
z
1
2
7
y
node x table
node y table
node z table
Dz(x) = min{c(z,x) + Dx(x), c(z,y) + Dy(x)} = min{7+0 , 1+2} = 3
Dz(y) = min{c(z,x) + Dx(y), c(z,y) + Dy(y)}
= min{7+2 , 1+0} = 1
3
2
x y z
x
y
z
0 2 7
1
7 1 0
2
0
x y z
x
y
z
0 2 7
from
2 0 1
from
3
1
0

## Slide 23
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
2 0 1
7 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
time
x
z
1
2
7
y
node x table
node y table
node z table

## Slide 24: Example
How many iterations are needed to make the final routing tables of each router?
What will be the routing table of B and D after the 2nd iteration?

## Slide 25: Network Layer Routing Algorithm Distance Vector Routing
Lecture 13 | Part 2| CSE421 – Computer Networks
Department of Computer Science and Engineering School of Data & Science

## Slide 26: Operation of Distance Vector
Periodic Updates:
  Periodically broadcast the entire routing table to each of its neighbors (RIP – every 30 seconds).
      Inefficient
  Router is only aware of the:
      Network addresses of its own interfaces.
      Network addresses the neighbors running the same routing protocol.
Notes:       Inefficient: Updates consume bandwidth and router CPU resources.
      Periodic updates are always sent even there have been no changes for weeks or months.

## Slide 27: Operation of Distance Vector
Periodic Updates:
R1 Update Timer expires
Neighbour of R1
Neighbour of R1
R1 is unaware of R3 and its networks
Updates sent.
Broadcast!

## Slide 28: Distance Vector Routing Protocols
Network Discovery

## Slide 29: Cold Start
Network Discovery:
  Is part of the process of the routing protocol algorithm that enables routers to learn about remote networks for the first time.

## Slide 30: Cold Start
When a router powers up:
  Knows nothing about the network topology.
  Knows only the information saved in NVRAM.
  Sends updates about its known networks out all ports.

## Slide 31: Initial Exchange of Routing Information
Sends an update about network 10.1.0.0 out the Serial 0/0/0 interface with a metric of 1.
Sends an update about network 10.2.0.0 out the Fa0/0 interface with a metric of 1.
10.1.0.0

## Slide 32: Initial Exchange of Routing Information
10.1.0.0
10.3.0.0
10.2.0.0
Notes:   Sends an update about network 10.3.0.0 out the Serial 0/0/0 interface with a metric of 1.
  Sends an update about network 10.2.0.0 out the Serial 0/0/1 interface with a metric of 1.

## Slide 33: Initial Exchange of Routing Information
10.1.0.0
10.3.0.0
10.2.0.0
10.4.0.0
Notes: Sends an update about network 10.4.0.0 out the S0/0/0 interface with a metric of 1.
Sends an update about network 10.3.0.0 out the Fa0/0 interface with a metric of 1.

## Slide 34: Initial Exchange of Routing Information
  R1 Receives the update from R2 about network 10.3.0.0 and adds it to its routing table.
  R3 Receives the update from R2 about network 10.2.0.0 and adds it to its routing table.
10.3.0.0
10.2.0.0

## Slide 35: Initial Exchange of Routing Information
  R2 Receives the update from R1 about network 10.1.0.0 and adds it to its routing table.
  R2 Receives the update from R3 about network 10.4.0.0 and adds it to its routing table.
10.1.0.0
10.4.0.0

## Slide 36: Next Exchange of Routing Information
Sends an update about network 10.1.0.0 out the S0/0/0 interface with a metric of 1 - AGAIN!
When R2 receives the update, there is no change in information so the update is ignored.
10.1.0.0

## Slide 37: Next Exchange of Routing Information
Sends an update about networks 10.3.0.0 with a metric of 1 and 10.4.0.0 with a metric of 2 out the Serial 0/0/0 interface.
Similarly sends updates about networks 10.1.0.0 with a metric of 2 and 10.2.0.0 with a metric of 1 out the Serial 0/0/1 interface.
10.4.0.0
10.3.0.0
10.2.0.0
10.1.0.0
NEW
NEW

## Slide 38: Next Exchange of Routing Information
10.4.0.0
Sends an update about network 10.4.0.0 out the S0/0/0 interface with a metric of 1 - AGAIN!
When R2 receives the update, there is no change in information so the update is ignored.

## Slide 39: Next Exchange of Routing Information
  R1 receives an update from R2 about network 10.3.0.0 and there is no change – update ignored.
  R1 receives an update from R2 about network 10.4.0.0 (new) and adds it to its routing table.
10.4.0.0
10.3.0.0

## Slide 40: Next Exchange of Routing Information
  R3 receives an update from R2 about network 10.2.0.0 and there is no change – update ignored.
  R3 receives an update from R2 about network 10.1.0.0 (new) and adds it to its routing table.
10.2.0.0
10.1.0.0

## Slide 41: Next Exchange of Routing Information
  The network has CONVERGED!
    All routers now know about all of the networks attached to all of their neighbouring routers.

## Slide 42: Convergence
The amount of time it takes for a network to converge is directly proportional to the size of that network.
Routing protocols are compared based on how fast they can propagate this information - their speed to convergence.
A network is not completely operable until it has converged.
  Network administrators prefer routing protocols with shorter convergence times.

## Slide 43: THE END