## Slide 1: Data Link Layer
Lecture 17 | Part 1 | CSE421 –Computer Networks
Department of Computer Science and Engineering School of Data & Science

## Slide 2
Computer Networking: A Top Down Approach
All material copyright 1996-2016
J.F Kurose and K.W. Ross, All Rights Reserved
7th edition Jim Kurose, Keith Ross Pearson/Addison Wesley April 2016
Chapter 6 The Link Layer and LANs

## Slide 3
Our objectives:
Link Layer Addressing
ARP
LAN Protocol
  Ethernet
LAN Switch
Objectives

## Slide 4
Our objectives:
Link Layer Addressing
  MAC Address
  Types of MAC Addresses
ARP
ARP within LAN
Objectives of Part 1&2

## Slide 5: Link Layer Addressing

## Slide 6: IP Address vs MAC Address
IP address
32 bits
Dotted decimal notation
  Example : 192.168.10.1
Network-layer address for interface
Hierarchal
  Not portable
Function
MAC address
48 bits
12 Hexadecimal digits
  Example : 1A-2F-BB-76-09-AD
Data Link-layer address for interface
Flat
  portable
Function

## Slide 7: MAC or LAN or Physical or Ethernet addresses (more)
48 bits MAC address (for most LANs) burned in NIC ROM, also sometimes software settable
MAC address allocation administered by IEEE
Manufacturer buys portion of MAC address space (to assure uniqueness)
Analogy:
  MAC address: like National ID
  IP address: like Postal Address

## Slide 8: MAC Address
  48 bits MAC address (for most LANs) burned in NIC ROM, also sometimes software settable
hexadecimal (base 16) notation
(each “numeral” represents 4 bits)
0000
1100

## Slide 9: Types of MAC Address
MAC Address
Unicast
Multcast
Broadcast

## Slide 10: Unicast MAC Addresses
The unique address used when a frame is sent from a single transmitting device to a single destination device.

## Slide 11: Multicast MAC Addresses
“ 01-00-5E” in an IPv4 multicast packet

## Slide 12: Broadcast MAC Address
A destination MAC address of FF-FF-FF-FF-FF-FF
To be processed by all devices in the network

## Slide 13: LAN addresses and ARP
each adapter on LAN has unique LAN address
adapter
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
(wired or
wireless)

## Slide 14: ARP: address resolution protocol
ARP
Mapping _IP Add___ to _MAC Add____
ARP table
  IP
  MAC address
  TTL (Time To Live) Or Age
    time after which address mapping will be forgotten (typically 20 min)
Question: how to determine
interface’s MAC address, knowing its IP address?
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
137.196.7.23
137.196.7.78
137.196.7.14
137.196.7.88

## Slide 15: ARP Tables
Host or PC
Router

## Slide 16: ARP: address resolution protocol
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
137.196.7.23
137.196.7.78
137.196.7.14
137.196.7.88
LAN
A
B
 | 71-65-F7-2B-08-53 | 137.196.7.14 | 137.196.7.23 | ARP Request
71-65-F7-2B-08-53 | 58-23-D7-FA-20-B0 | 137.196.7.23 | 137.196.7.14 | ARP Reply
Dest MAC | Source MAC | Dest IP Add | Source IP Add | ARP Req/Reply
ARP
FF-FF-FF-FF-FF-FF
ARP
ARP
ARP
X
X
✔️
ARP Reply
A wants to send datagram to B

## Slide 17: ARP protocol: same LAN
A wants to send datagram to B
  B’s MAC address not in A’s ARP table.
A broadcasts ARP query packet, containing B's IP address
  destination MAC address = FF-FF-FF-FF-FF-FF
  all nodes on LAN receive ARP query
B receives ARP packet, replies to A with its (B's) MAC address
  frame sent to A’s MAC address (unicast)
A caches (saves) IP-to-MAC address pair in its ARP table
  Soft state: information that times out (goes away) unless refreshed
ARP is “plug-and-play”:
  nodes create their ARP tables without intervention from net administrator
Notes: until information becomes old (times out)

## Slide 18
Our objectives:
ARP
  when sending outside own LAN or sending a packet to a different network.
Objectives of Part 3

## Slide 19: Addressing: routing to another LAN
Send datagram from A to B via R
  focus on addressing – at IP (datagram) and MAC layer (frame)
  assume A knows B’s IP address
  What will be the destination MAC Address?
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
 |  | 222.222.222.222 | 111.111.111.111 | A to B Packet
Dest MAC | Source MAC | Dest IP Add | Source IP Add | Packet Type
74-29-9C-E8-FF-55
???
Routers never forward broadcast packets!
Default Gateway’s MAC Address
ARP- To know B’s MAC address as B’s IP address is known

## Slide 20: Addressing: routing to another LAN
Send datagram from A to B via R
  Does A know the IP address of first hop router, R which is also known as Default Gateway? (how?)
  Will A know R’s MAC address?
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
ARP
ARP
ARP
ARP Reply
 | 74-29-9C-E8-FF-55 | 222.222.222.222 | 111.111.111.111 | A to B Packet
E6-E9-00-17-BB-4B

## Slide 21: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP src: 111.111.111.111
IP dest: 222.222.222.222
A creates IP datagram with IP source A, destination B
A creates link-layer frame with R's MAC address as destination address, frame contains A-to-B IP datagram
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B

## Slide 22: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
frame sent from A to R
IP
Eth
Phy
frame received at R, datagram removed, passed up to IP
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B
IP src: 111.111.111.111
IP dest: 222.222.222.222
IP src: 111.111.111.111
IP dest: 222.222.222.222

## Slide 23: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP src: 111.111.111.111
IP dest: 222.222.222.222
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as destination address, frame contains A-to-B IP datagram
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy
ARP
ARP
ARP Reply
ARP

## Slide 24: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as destination address, frame contains A-to-B IP datagram
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy

## Slide 25: Addressing: routing to another LAN
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
R forwards datagram with IP source A, destination B
R creates link-layer frame with B's MAC address as dest, frame contains A-to-B IP datagram
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 26
Our objectives:
LAN Protocol : Ethernet
  Ethernet Frame Structure
  Features of Ethernet
  Types of Ethernet
Objectives of Part 4

## Slide 27: Ethernet
“Dominant” wired LAN technology
Cheap
First
Simple
Fast : 10 Mbps – 10 Gbps
Metcalfe’s Ethernet sketch

## Slide 28: Ethernet: physical topology
Bus
popular through mid 90s
  All nodes in same collision domain
bus: coaxial cable
star
switch
Star
prevails today
  Active switch in center
  Nodes do not collide with each other

## Slide 29: Ethernet Frame Structure
Ethernet Frame
  Sending adapter encapsulates IP datagram (or other network layer protocol packet) with header and trailer
Header | Data | Trailer
Header
Trailer
46 -1500 bytes

## Slide 30: Ethernet Frame Structure
Preamble:
7 bytes
Six 10101010 patterns
One 10101011 pattern
used to synchronize receiver, sender clock rates
Preamble
Source
Address
Dest
Address
Type
Data
CRC

## Slide 31: Ethernet Frame Structure
Preamble
Source
Address
Dest
Address
Type
Data
CRC
Destination and Source addresses
  6 bytes source & destination MAC addresses
Type
  Indicates higher layer protocol (E.g. mostly IP)
  Allows to multiplex network layer protocols or ARP
Notes:   if adapter receives frame with matching destination address, or with broadcast address (e.g. ARP packet), it passes data in frame to network layer protocol
  otherwise, adapter discards frame

## Slide 32: Ethernet Frame Structure
Preamble
Source
Address
Dest
Address
Type
Data
CRC
Data field
  Contains IP datagram
  Min 46 bytes and max 1500 bytes
CRC
  Cyclic redundancy check at receiver
  error detected: frame is dropped
Notes:   if adapter receives frame with matching destination address, or with broadcast address (e.g. ARP packet), it passes data in frame to network layer protocol
  otherwise, adapter discards frame

## Slide 33: Ethernet: unreliable, connectionless
Connectionless: no handshaking between sending and receiving NICs
unreliable: receiving NIC doesn't send acks or nacks to sending NIC
  data in dropped frames recovered only if initial sender uses higher layer rdt (e.g., TCP), otherwise dropped data lost
Ethernet’s MAC protocol: unslotted CSMA/CD with binary backoff

## Slide 34: 802.3 Ethernet standards: link & physical layers
Many different Ethernet standards
  common MAC protocol and frame format
  different speeds: 2 Mbps, 10 Mbps, 100 Mbps, 1Gbps, 10 Gbps, 40 Gbps
  different physical layer media: fiber, cable
application
transport
network
link
physical
MAC protocol
and frame format
100BASE-TX
100BASE-T4
100BASE-FX
100BASE-T2
100BASE-SX
100BASE-BX
fiber physical layer
copper (twister
pair) physical layer

## Slide 36
Our objectives:
Switch
  Characteristics of a switch
  Role of switch in a LAN
Objectives of Part 5

## Slide 37: Ethernet switch
link-layer device: takes an active role
  store, forward Ethernet frames
  examine incoming frame’s MAC address, selectively forward frame to one-or-more outgoing links when frame is to be forwarded on segment, uses CSMA/CD to access segment
transparent
  hosts are unaware of presence of switches
plug-and-play, self-learning
  switches do not need to be configured

## Slide 38: Switch: multiple simultaneous transmissions
hosts have dedicated, direct connection to switch
switches buffer packets
Ethernet protocol used on each incoming link, but no collisions; full duplex
  each link is its own collision domain
switching: A-to-A’ and B-to-B’ can transmit simultaneously, without collisions
switch with six interfaces
(1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6

## Slide 39: Switch forwarding table
Q: how does switch know A’ reachable via interface 4, B’ reachable via interface 5?
switch with six interfaces
(1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6
A: each switch has a switch table, each entry:
  (MAC address of host, interface to reach host, time stamp)
  looks like a routing table!
Q: how are entries created, maintained in switch table?
  something like a routing protocol?

## Slide 40: Switch: self-learning
A
A’
B
B’
C
C’
1
2
3
4
5
6
switch learns which hosts can be reached through which interfaces
  when frame received, switch “learns” location of sender: incoming LAN segment
  records sender/location pair in switch table
A A’
Source: A
Dest: A’
MAC addr interface TTL
Switch table
(initially empty)
A
1
60

## Slide 41: Switch: frame filtering/forwarding
when frame received at switch:
  1. record incoming link, MAC address of sending host
  2. index switch table using MAC destination address
  3. if entry found for destination then {
  if destination on segment from which frame arrived then drop frame
  else forward frame on interface indicated by entry
  }
  else flood /* forward on all interfaces except arriving
  interface */

## Slide 42: Self-learning, forwarding: example
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
MAC addr interface TTL
switch table
(initially empty)
A
1
60
A A’
A A’
A A’
A A’
A A’
frame destination, A’, location unknown:
flood
A’ A
destination A location known:
A’
4
60
selectively send
on just one link

## Slide 43: Interconnecting switches
self-learning switches can be connected together:
Q: sending from A to G - how does S1 know to forward frame destined to G via S4 and S3?
A: self learning! (works exactly the same as in single-switch case!)
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G

## Slide 44: Self-learning multi-switch example
Suppose C sends frame to I, I responds to C
Q: show switch tables and packet forwarding in S1, S2, S3, S4
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G

## Slide 45: Institutional network
to external
network
router
IP subnet
mail server
web server

## Slide 46: Switches vs. routers
both are store-and-forward:
routers: network-layer devices (examine network-layer headers)
switches: link-layer devices (examine link-layer headers)
both have forwarding tables:
routers: compute tables using routing algorithms, IP addresses
switches: learn forwarding table using flooding, learning, MAC addresses
application
transport
network
link
physical
network
link
physical
link
physical
switch
datagram
application
transport
network
link
physical
frame
frame
frame
datagram

## Slide 47: THE END!