## Slide 1: CSE460: VLSI Design
Lecture 2

## Slide 2: Review of digital logic design

## Slide 3: Background
Logic gates (AND, OR, NOT, XOR, etc.)
Boolean algebra
Truth tables
Logic functions
Logic function synthesis by
  Sum of Products (SOP)
  Product of Sums (POS)
  K-maps
Logic blocks (MUX, DEMUX)
Sequential elements (Latch, Flip-flop)

## Slide 4: Logic gates

## Slide 5: Generalized n-input logic gates

## Slide 6: Axioms of Boolean Algebra
1a. 0 · 0 = 0
1b. 1 + 1 = 1
2a. 1 · 1 = 1
2b. 0 + 0 = 0
3a. 0 · 1 = 1 · 0 = 0
3b. 1 + 0 = 0 + 1 = 1
4a. If x = 0, then x’ = 1
4b. If x = 1, then x’ = 0

## Slide 7: Boolean Algebra - Single Variable Theorems
5a. x · 0 = 0
5b. x + 1 = 1
6a. x · 1 = x
6b. x + 0 = x
7a. x · x = x
7b. x + x = x
8a. x · x’ = 0
8b. x + x’ = 1
9. (x’)’ = x

## Slide 8: Boolean Algebra - Two Variable Properties
10a. x · y = y · x Commutative
10b. x + y = y + x
11a. x · ( y · z) = (x · y) · z Associative
11b. x + ( y + z) = (x + y) + z
12a. x · ( y + z) = x · y + x · z Distributive
12b. x + y · z = (x + y) · (x + z)
13a. x + x · y = x Absorption
13b. x · (x + y) = x
14a. x · y + x · y’ = x Combining
14b. (x + y) · (x + y’) = x

## Slide 9: Boolean Algebra - Two & Three Variable Properties
15a. (x · y)’ = x’ + y’ DeMorgan’s theorem
15b. (x + y)’ = x’ · y’
16a. x + x’ · y = x + y
16b. x · (x + y) = x · y
17a. x · y + y · z + x’ · z = x · y + x’ · z Consensus
17b. (x + y) · (y + z) · (x’ + z) = (x + y) · (x’ + z)

## Slide 10: Logic Function Synthesis - Three variable SOP & POS
Function synthesis from truth table

## Slide 11: Logic Function Synthesis - 2/3/4 variable k-map
Function synthesis using k-maps

## Slide 12: Multiplexer
Multiple inputs, single output. Output is chosen by selector pin/s

## Slide 13: D Latch
Level sensitive element
A positive level triggered D latch
  copies D to output Q, if Clock=1, else preserves the previous output
A negative level triggered D latch
  copies D to output Q, if Clock=0, else preserves the previous output

## Slide 14: D Flip-flop
Edge sensitive element
A positive edge triggered D flip-flop
  Sets Q=D at all positive edges (rising edges) of the clock, retains the old value of Q otherwise
A negative edge triggered D flip-flop
  Sets Q=D at all negative edges (falling edges) of the clock, retains the old value of Q otherwise

## Slide 15: Building D Flip-flops using D Latches
By cascading a positive level triggered D latch and a negative level triggered D latch we can build a negative edge triggered D flip-flop

## Slide 16: Level triggered vs. Edge triggered
In level triggered elements
  output is affected by the clock levels (high/low)
In edge triggered elements
  output is affected by the clock edges (positive edge/negative edge) (rising edge/falling edge)

## Slide 17: Slide references
https://instrumentationtools.com/logic-gates/
Stephen Brown & Zvonko Vranesic - Fundamentals of Digital Logic with Verilog Design

## Slide 18: Thank you!