## Slide 1: Data Link Layer
Lecture 16 | Part 1 of 5 | CSE421 –Computer Networks
Department of Computer Science and Engineering School of Data & Science

## Slide 2
Computer Networking: A Top Down Approach
All material copyright 1996-2016
J.F Kurose and K.W. Ross, All Rights Reserved
7th edition Jim Kurose, Keith Ross Pearson/Addison Wesley April 2016
Based on Chapter 6 The Link Layer and LANs
The slides are adapted from Kurose and Ross, Computer Networks 7th edition, Kurose and Ross.

## Slide 3: Chapter 6: Link layer and LANs
Our objectives:
understand principles behind link layer services:
  error detection, correction (done in CSE320)
  sharing a broadcast channel: multiple access
  Framing - link layer addressing
  local area networks: Ethernet

## Slide 4: Part - 1
Introduction to Link Layer
Application
Presentation
Session
Transport
Network
Data link
Physical

## Slide 5: Link Layer Terminology
Nodes : hosts and routers
Links:
  wired links
  wireless links
Frame : layer-2 packet
data-link layer has responsibility of
transferring datagram from one node
to physically adjacent node over a link

## Slide 6: Link layer: context
datagram transferred by different link protocols over different links:
  e.g., Ethernet on first link, frame relay on intermediate links, 802.11 on last link
each link protocol provides different services
Ethernet
WAN Protocol : Frame Relay
Ethernet
802.11
Transportation analogy:
trip from Home to Cox’s Bazaar
  Uber Car : Home to Dhaka Airport
  Plane: Dhaka to Chittagong
  Bus: Chittagong to Cox’s Bazaar
tourist = datagram
transport segment = communication link
transportation mode = link layer protocol
travel agent = routing algorithm

## Slide 7: Link layer services
Framing
  encapsulate datagram into frame, adding header, trailer
  “MAC” addresses used in frame headers to identify source, destination
    different from IP address!
Link access:
  channel access if shared medium
Reliable delivery between adjacent nodes
  we learned how to do this already (Transport Layer)
  seldom used on low bit-error link (fiber, some twisted pair)
  wireless links: high error rates
    Q: why both link-level and end-end reliability?

## Slide 8: Link layer services (more)
error detection:
  errors caused by signal attenuation, noise.
  receiver detects presence of errors:
    signals sender for retransmission or drops frame
error correction:
  receiver identifies and corrects bit error(s) without resorting to retransmission
flow control:
  pacing between adjacent sending and receiving nodes
half-duplex and full-duplex
  with half duplex, nodes at both ends of link can transmit, but not at same time

## Slide 9: Where is the link layer implemented?
in each and every host
link layer implemented in “adaptor” (aka network interface card NIC) or on a chip
  Ethernet card, 802.11 card; Ethernet chipset
  implements link, physical layer
attaches into host’s system buses
combination of hardware, software, firmware
controller
physical
transmission
cpu
memory
host
bus
(e.g., PCI)
network adapter
card
application
transport
network
link
link
physical

## Slide 10: Adaptors communicating
sending side:
  encapsulates datagram in frame
  adds error checking bits, rdt, flow control, etc.
receiving side
  looks for errors, rdt, flow control, etc.
  extracts datagram, passes to upper layer at receiving side
controller
controller
sending host
receiving host
datagram
datagram
datagram
frame

## Slide 11: Objectives of Part 2
Our Objectives:
Types of Links
Multi Access Protocols
Types of Multi Access Protocols
  Channel Partitioning Protocols
  Random Access protocols
  Taking Turns Protocols

## Slide 12: Links
Links
Point-to-point
Broadcast
point-to-point
  Example :Router to router connection
  Example protocols : PPP, HDLC

## Slide 13: Multiple access links, protocols
broadcast (shared wire or medium)
  old-fashioned Ethernet
  upstream satellite network
  802.11 wireless LAN
shared wire (e.g.,
cabled Ethernet)
shared RF
(satellite)
humans at a
party
(shared air, acoustical)
wireless LAN

## Slide 14: Multiple access link problems
BOOM!
Problem
  Single shared broadcast channel
  Collision

## Slide 15: Multiple access protocols
Solution:
Multiple access protocol
distributed algorithm that determines how nodes share channel, i.e., determine when node can transmit

## Slide 16: An ideal multiple access protocol
given: broadcast channel of rate R bps
desiderata:
  1. Efficient :when one node wants to transmit, it can send at rate R.
  2. Fair : when M nodes want to transmit, each can send at average rate R/M
  3. Fully decentralized:
    no special node to coordinate transmissions
    no synchronization of clocks, slots
  4. Simple

## Slide 17: MAC protocols: types
MAC Protocols
Channel Partitioning
Random Access
Taking Turns
divide channel into smaller “pieces” (time slots, frequency, code)
allocate piece to node for exclusive use
channel not divided, allow collisions
“recover” from collisions
nodes take turns, but nodes with more to send can take longer turns

## Slide 18: Channel Partitioning MAC Protocols
Time Division Multiple Access
Frequency Division Multiple Access
Code Division Multiple Access

## Slide 19
TDMA divides divides the time frames into time slots.
Each slot is assigned to one of the nodes.
Slots sizes are usually the same as the packet (frame) size of node.
Advantages
  Eliminates collision
  Each node gets dedicated R/N bps during frame time.
TDMA: Time Division Multiple Access
Frequency

## Slide 20: Channel partitioning MAC protocols: TDMA
Disadvantages:
Unused slots go idle
Example: 6-station LAN, 1,3,4 have packets to send, slots 2,5,6 idle
When there is only one node to transmit
  Then the node is limited to an average rate of R/N bps
  The node must wait for it’s turn to transmit
1
3
4
1
3
4
6-slot
frame
6-slot
frame

## Slide 21: FDMA: Frequency Division Multiple Access
channel spectrum divided into frequency bands
each station assigned fixed frequency band
Disadvantage
unused transmission time in frequency bands go idle
  example: only band 1 have packet to send, frequency bands 2 & 3 remains idle
Limited bandwidth of R/N for each node
f3
f2
f1
Frequency
Time

## Slide 22
Assigns a different code to each node.
Each node then uses its unique code to encode the data bits it sends.
CDMA: Code Division Multiple Access
Disadvantage
Total frequency band is used inefficiently.

## Slide 23: Objectives of Part 3
Our objectives:
understand Random Access Protocols:
  slotted ALOHA
  ALOHA
  CSMA, CSMA/CD

## Slide 24: Random access protocols
when node has packet to send
  transmit at full channel data rate R.
  no previous coordination among nodes
two or more transmitting nodes ➜ “collision”,
random access MAC protocol specifies:
  how to detect collisions
  how to recover from collisions (e.g., via delayed retransmissions)

## Slide 25: Random access protocols
Types of random access MAC protocols:
  slotted ALOHA
  ALOHA
  CSMA, CSMA/CD, CSMA/CA

## Slide 26: Slotted ALOHA
Assumptions:
All frames same size
Time divided into equal size slots
Nodes start to transmit only slot beginning
If 2 or more nodes transmit in slot, all nodes detect collision
Operation:
Transmits in next slot
if no collision: node can send new frame in next slot
if collision: node retransmits frame in each subsequent slot with prob. p until success

## Slide 27: Example
Frame can be sent
Frame cannot be sent
10 sided dice
P=50%
P=10%

## Slide 28: Slotted ALOHA
Pros:
single active node can continuously transmit at full rate of channel
highly decentralized: only slots in nodes need to be in sync
simple
Cons:
collisions, wasting slots
idle slots
nodes may be able to detect collision in less than time to transmit packet
clock synchronization
1
1
1
1
2
3
2
2
3
3
node 1
node 2
node 3
C
C
C
S
S
S
E
E
E

## Slide 29: Slotted ALOHA: efficiency
Efficiency:
Fraction of successful slots
Suppose:
N nodes with many frames to send, each transmits in slot with probability p
prob that given node has success in a slot = p(1-p)N-1
prob that any node has a success = Np(1-p)N-1
Maximum Efficiency
Find p* that maximizes Np(1-p)N-1
Find the limit of Np*(1-p*)N-1 as N goes to infinity, gives:
Max efficiency = 1/e = 0.37

## Slide 30: Pure (unslotted) ALOHA
unslotted Aloha: simpler, no synchronization
when frame first arrives
  transmit immediately
collision probability increases:
  frame sent at t0 collides with other frames sent in [t0-1,t0+1]

## Slide 31: Pure ALOHA efficiency
P(success by given node) = P(node transmits) .
P(no other node transmits in [t0-1,t0] .
P(no other node transmits in [t0-1,t0]
= p . (1-p)N-1 . (1-p)N-1
= p . (1-p)2(N-1)
… choosing optimum p and then letting n
= 1/(2e) = .18
even worse than slotted Aloha!

## Slide 32: Objectives of Part 4
Our objectives:
understand Random Access Protocols:
  slotted ALOHA
  ALOHA
  CSMA, CSMA/CD

## Slide 33: CSMA (carrier sense multiple access)
CSMA: listen before transmit:
if channel sensed idle
  transmit entire frame
if channel sensed busy
  defer transmission
human analogy: don’t interrupt others!

## Slide 34: CSMA collisions
Collisions can still occur: propagation delay means two nodes may not hear each other’s transmission
Collision: entire packet transmission time wasted
  distance & propagation delay play role in in determining collision probability
spatial layout of nodes

## Slide 35: CSMA/CD (collision detection)
CSMA/CD: carrier sensing, deferral as in CSMA
  collisions detected within short time
  colliding transmissions aborted, reducing channel wastage
collision detection:
  easy in wired LANs: measure signal strengths, compare transmitted, received signals
  difficult in wireless LANs: received signal strength overwhelmed by local transmission strength

## Slide 36: CSMA/CD (collision detection)
spatial layout of nodes

## Slide 37: Ethernet CSMA/CD algorithm
1. NIC receives datagram from network layer, creates frame
2. If NIC senses channel idle, starts frame transmission. If NIC senses channel busy, waits until channel idle, then transmits.
3. If NIC transmits entire frame without detecting another transmission, NIC is done with frame !
4. If NIC detects another transmission while transmitting, aborts and sends jam signal
5. After aborting, NIC enters binary (exponential) backoff:

## Slide 38: CSMA/CD efficiency
tprop = max prop delay between 2 nodes in LAN
ttrans = time to transmit max-size frame
efficiency goes to 1
  as tprop goes to 0
  as ttrans goes to infinity
Better performance than ALOHA: and simple, cheap, decentralized!

## Slide 39: Objectives : Part 5
Our Objectives:
understand principles behind Toking Turns Protocols
  Polling
  Token Passing

## Slide 40: MAC protocols
MAC Protocols
Channel Partitioning
Random Access
Taking Turns
Efficient and fair at High load
Inefficient at low load
Efficient at Low Load
Inefficient at high load
Best of both worlds?

## Slide 41: “Taking turns” MAC protocols
Polling:
master node “invites” slave nodes to transmit in turn
typically used with “dumb” slave devices
Concerns:
  polling overhead
  latency
  single point of failure (master)
master
slaves
poll
data
data

## Slide 42: “Taking turns” MAC protocols
Token passing:
token message
control token passed from one node to next sequentially.
Concerns:
  token overhead
  latency
  single point of failure (token)
T
data
(nothing
to send)
T

## Slide 43: Summary of MAC protocols
channel partitioning, by time, frequency or code
  Time Division, Frequency Division
random access (dynamic),
  ALOHA, S-ALOHA, CSMA, CSMA/CD
  carrier sensing: easy in some technologies (wire), hard in others (wireless)
  CSMA/CD used in Ethernet
  CSMA/CA used in 802.11
taking turns
  polling from central site, token passing
  Bluetooth, FDDI, token ring

## Slide 44: THE END!