## Slide 1: Transport Layer (TCP)
Lecture 7 | Parts 1 to 5 | CSE421 – Computer Networks
Department of Computer Science and Engineering School of Data & Science

## Slide 2: TCP Services
Stream delivery
Segmenting and Reassembling segments
Multiplexing segments
Full Duplex Service
Identifying and tracking the segments of different applications
Connection Oriented Service
Reliable service

## Slide 3: Objectives of Part 1
Stream delivery
Segmenting and Reassembling segments
Multiplexing segments
Full Duplex Service
Identifying and tracking the segments of different applications.

## Slide 4: Stream Delivery
TCP, unlike UDP, is a stream-oriented protocol
TCP allows the sending process to deliver data as a stream of bytes
And allows the receiving process to obtain data as a stream of bytes

## Slide 5: Buffers
The sending and the receiving processes may not necessarily write or read
data at the same rate
So TCP will need to store the data in a place before it can process it.
That storage space is known as buffer

## Slide 6: Segments
The network layer, as a service provider for TCP, needs to send data in packets, not as a stream of bytes.
So TCP groups a number of bytes together into a packet called a segment .

## Slide 7: TCP Segment Reassembly

## Slide 8: Multiplexing
Like UDP, TCP performs multiplexing at the sender and demultiplexing at the receiver

## Slide 9: Full Duplex
Each TCP connection supports a pair of byte streams, one flowing in each direction.
Exchanging data (sending and receiving) between two entities at the same time.

## Slide 10: Identifying and tracking the segments
TCP and UDP-based services must keep track of the various applications communicating.
To differentiate the segments and datagrams for each application, both TCP and UDP uses port numbers.

## Slide 11: Objectives of Part 2
TCP Segment Header
  All header fields

## Slide 12
TCP Segment Header

## Slide 13: Byte Number
The bytes of data being transferred in each connection are numbered by TCP.
The numbering starts with an arbitrarily generated number.
An arbitrary number between 0 and 232 − 1 for the number of the first byte.
For example if the number of the first byte happens to be 1067 and the total data to be sent is 3000 bytes .
What is the byte number for the first byte of data and last byte of data?
First Byte Number
1067
Last Byte Number
4066

## Slide 14: Sequence Numbers
The sequence number of the first segment is the ISN (initial sequence number), which is a random number (byte number).
The sequence number of any other segment is the sequence number of the previous segment plus the number of bytes (real or imaginary) carried by the previous segment.
Suppose a TCP connection is transferring a file of 5,000 bytes. The first byte is numbered 10,001. What are the sequence numbers for each segment if data are sent in five segments, each carrying 1,000 bytes?
Solution:

## Slide 15
Expectational Acknowledgement
Acknowledgement Number
If receiving host TCP receives uncorrupted data, then…
It sends an acknowledgement by giving the sequence number of the byte that it expects next.

## Slide 16: Acknowledgement Number
The value of the acknowledgment field in a segment defines the number of the next byte the receiver expects to receive.
The acknowledgment number is cumulative.
For example if the sender receives 1001 as the acknowledgement number.
What does it mean?
Received all data up to
1000, tells the sender that it ready to receive the next data from 1001 byte number.
Note :This does not indicate receiver has received 1000 bytes of data. Why?

## Slide 17: Acknowledgement Number
The acknowledgment number is cumulative.
Receiver acknowledges multiple data segments in one acknowledgement.
Sender
Receiver

## Slide 18: Header Length
Header Length :
  Indicates the number of 4-byte words
  The length of the header can be between 20 and 60 bytes

## Slide 19: Control Bits
Control Bits:
  This field defines 6 different control bits or flags
  One or more of these bits can be set at a time
  These bits help indicate connection establishment and termination, flow control

## Slide 20: Window Size
Window Size:
  This field defines size of data in bytes of the sending TCP process
  The maximum size of the window is 65,535 bytes
  Normally referred to as the receiving window (rwnd )
  The sender must obey the dictation of the receiver in this case

## Slide 21: Checksum
This 16 bits field is used to check if the segment got corrupted (intentionally or unintentionally) while segment was on traveling in order to reach the destination.
Mandatory in TCP
TCP Header
TCP Body
Pseudo IP Header

## Slide 22: Urgent Pointer
This 16-bit field, which is valid only if the urgent flag is set.
Used when the segment contains urgent data.
It defines a value that must be added to the sequence number to obtain the number of the last urgent byte in the data section of the segment.
1500
1500
1oo1

## Slide 23: Options
  There can be up to 40 bytes of optional information in the TCP header
  Provides a way to deal with limitations of the original header
  For example :
    MSS (Maximum Segment Size) is defined as the largest block of data that a sender using TCP will send to the receiver

## Slide 24: Objectives of Part 3
TCP Services
  Connection Establishment
  Pushing Data
  Connection Termination

## Slide 25: Connection Establishment
TCP sets up a connection between end hosts before sending data
This process is known as ”Three-way handshake”
After the connection is established the hosts can send data

## Slide 26
Source Port No. |  |  |  |  |  | Destination Port No. | 
Sequence No. |  |  |  |  |  |  | 
Acknowledgement No. |  |  |  |  |  |  | 
 | U | A | P | R | S | F | Window Size
Others |  |  |  |  |  |  | 
80
49152
 |  |  |  |  |  |  | Window Size
Others |  |  |  |  |  |  | 
49152
80
100
0
S
80
49152
0
101
S
A
80
49152
101
1
A
3 Way Handshake : Connection Establishment

## Slide 27
3 Way Handshake : Connection Establishment

## Slide 28
Data Transfer

## Slide 29
Data Transfer Continued..

## Slide 30: Connection Termination

## Slide 31
3 Way Handshake : Connection Termination

## Slide 32: Connection Termination :: Half Close

## Slide 33: Objectives Part 4
Reliable service
  Error Control

## Slide 34: Reliability in TCP
TCP provides reliability using error control
Error control includes mechanisms for
  detecting and resending corrupted segments
  resending lost segments
  storing out-of order segments until missing segments arrive
  detecting and discarding duplicated segments.
Error control in TCP is achieved through
  Checksum
  Acknowledgment
  Time-out and retransmission

## Slide 35: Error Control
Checksum
  Each segment includes a checksum field, which is used to check for a corrupted segment
  If a segment is corrupted, as detected by an invalid checksum, the segment is discarded
Acknowledgment
  To confirm the receipt of data segments.
  To confirm control segments that carry no data, but consume a sequence number
ACK segments do not consume sequence numbers and are not acknowledged.

## Slide 36: Types and Rules of Acknowledgment
Cumulative Acknowledgment (ACK)
Selective Acknowledgment (SACK)
Generating Acknowledgments Rules (1 to 3)
  Rule 1: When host A sends a data segment to host B, it must include (piggyback) an acknowledgment number.
  Rule 2 : The receiver needs to delay sending an ACK segment if there is only one outstanding in-order segment.
  Rule 3: When a segment arrives with a sequence number that is expected by the receiver, and the previous in-order segment has not been acknowledged, the receiver immediately sends an ACK segment.

## Slide 37
Normal Operation

## Slide 38
Segment Lost or Corrupted?
Retransmission of segment ??
How will the sender know ??
What about the receiver, not aware of a packet sent?
Retransmission after time out.
Other Scenarios

## Slide 39
The heart of the error control mechanism is the retransmission of segment
When a segment is sent, it is stored in a queue until it is acknowledged.
Retransmission of segment will occur
After RTO
  The sending TCP maintains one retransmission time-out (RTO) for each connection.
  When the timer matures TCP resends the segment in the front of the queue
After Three Duplicate ACK Segments
  If three duplicate acknowledgments (i.e., an original ACK plus three exactly identical copies) arrive for a segment, the next segment is retransmitted without waiting for the time-out.
Retransmission

## Slide 40: Out of Order Segments
TCP implementations today do not discard out-of-order segments.
They store them temporarily .
Flag them as out-of-order segments until the missing segments arrive.
Out-of-order segments are never delivered to the process.
TCP guarantees that data are delivered to the process in order.

## Slide 41: Rules of Acknowledgment contd
Generating Acknowledgments Rules (4 to 6)
Rule 4: When a segment arrives with an out-of-order higher sequence number the receiver immediately sends an ACK segment .
Rule 5 : When a missing segment arrives, the receiver sends an ACK segment to announce the next sequence number expected.
Rule 6: If a duplicate segment arrives, the receiver discards the segment, but immediately sends an acknowledgment indicating the next in-order segment expected.

## Slide 42
Lost Segment

## Slide 43
Fast Retransmission :: 3 Acks

## Slide 44
Lost Acknowledgement

## Slide 45
Lost Ack corrected by resending a segment

## Slide 46: Objectives – Part 5
Reliable service
  Flow Control
    Sliding Window Concept

## Slide 47: Flow Control
Transmission Control Protocol (TCP) uses a sliding window for flow control.
What is the “Window ”?
  Indicates the size of the device's receive buffer for the particular connection.
  How much data a device can handle from its peer at one time before it is passed to the application process.
  Set by receiver of data
  Example : The server's window size was 360. This means the receiver is willing to take no more than 360 bytes at a time from the sender.

## Slide 48
Flow Control

## Slide 49
. . . | 200 | 201 | . . . . . | 260 | 261 | . . . . . | 300 | 301 | . . .
Bytes that are acknowledged
Window Size = 100 bytes
Window Size as advertised by the receiver
Variables
Sf = 201
Sn = 261
Outstanding Bytes
sent but not acknowledged
First outstanding byte
Next byte to send
Sf
Sn
Bytes that cannot be sent
Bytes that can be sent (Usable window)
Sender Sliding Window

## Slide 50
Sliding of Sender Window

## Slide 51
. . . | 200 | 201 | . . . | 241 | 242 | . . . | 260 | 261 | . . . . . | 300 | 301 | . . .
Window Size = 100 bytes
Window Size as advertised by the receiver
Variables
Sf = 201
Sn = 261
Outstanding Bytes
sent but not acknowledged
First outstanding byte
Sf
Next byte to send
Sn
Bytes that cannot be sent
Bytes that can be sent (Usable window)
Bytes that are acknowledged
#Sender receives a segment with ACK 241
And rwnd = 60
First outstanding byte
Sf
Bytes that are acknowledged
Outstanding Bytes
sent but not acknowledged
340
rwnd = 100
Sliding of Sender Window
Variables
Sf = 241
Sn = 261

## Slide 52
. . . | 200 | 201 | . . . . . | 260 | 261 | . . . . . | 300 | 301 | . . .
Bytes that have already been pulled by the process
rwnd= buffer size – number of bytes to be pulled
Receive window and allocated buffer
Bytes received and acknowledged, waiting to be consumed by process
Next byte to be pulled by process
Next byte expected to receive
Rn
Bytes that cannot be received
Bytes that can be received from the sender
Receive window(rwnd)
Receiver Sliding Window
Window Size = 100 bytes
= 40 bytes

## Slide 53
Sliding of Receiver Window

## Slide 54: Flow Control Example

## Slide 55: Flow Control Example Contd

## Slide 56: Shrinking of Windows
The receive window cannot shrink
The send window can shrink if the receiver defines a such value for rwnd
However, some implementations do not allow shrinking of the send window
The receiver needs to keep the following relationship
new ackNo + new rwnd ≥ last ackNo + last rwnd

## Slide 57: Shrinking of Windows
new ackNo + new rwnd ≥ last ackNo + last rwnd

## Slide 58: Different TCP Sliding Window Protocols
Go Back N Protocol
  If the sent segment are are found corrupted or lost then all the segments are re-transmitted from the lost segment to the last segment transmitted
  Do not keep track of out of order segments
  Efficient for less noisy channel

## Slide 59: Different TCP Sliding Window Protocols
Selective Repeat Protocol
  Only those segments are re-transmitted which are found lost or corrupted
  Keep track of out of order segments at the receiver side
  More efficient for noisy channels
  Widely used in TCP

## Slide 60: Overall Flow control
The initial window size is agreed during the three-way handshake.
If this is too much for the receiver and it loses data (e.g. buffer overflow) then it can decrease the window size.
If all is well then the receiver will increase the window size.

## Slide 61: The End
Part 1-5